JACUSA Mini-Manual

$ java -jar jacusa.jar [-h | --help]
usage: jacusa <COMMAND> [OPTIONS] BAM1_1[,BAM1_2,...] BAM2_1[,BAM2_2,...]

commands:
* call-2:
variant calling for paired samples
* pileup
samtools like mpileup (base columns don't contain read start/end markers)

java -jar jacusa.jar <command> gives command specific help

General notes:
* BAM files must be indexed (samtools index)!
* Sequence dictionaries of BAM headers of each input file need to be identical!
* Don't start too many multi-threaded JACUSA instances → IO-intensive!
* Memory consumption depends on:
- # of parallel threads
- used filters
- --window-size command line option
- „2-3 GB per thread should be fine“

General workflow of JACUSA variant calling

Read BAM(s) 1
Candidates variants
Create Parallelpileup (window based)
Store Meta-information
(read position of variant, etc.)
Read BAM(s) 2

Filter reads (mapq, flags)
Fitler base calls (basq)
Read coverage
...

Output
Variants
Filtered
Variants

Use test-statistic to
identify variant candidates

Use Meta-information to
filter FP variants

Building Pileup(s):
JACUSA supports „arbitrary“ combinations of „stranded reads“ controlled by:
-P,--build-pileup <BUILD-PILEUP>	Choose how parallel pileups are build: strand specific	(S) or strand unspecific (U)
default: U,U
For semi-stranded cases (BUILD-PILEUP = S,U or U,S) strand information is used from the strands specific BAM files.

Sample specific option:
Some command line options can be set globally or per sample:
* min mapping quality (-m{1,2})
* min base call quality (-q{1,2})
* min read coverage (-c{1,2})
* max read coverage (-d{1,2})

Filtering potential variants:
-a,--pileup-filter <PILEUP-FILTER>	chain of PILEUP-FILTER to apply to pileups:
Filters are separated by ','. Some filters allow to change default values. A simple format is used to override default values, separated by ':' (<FILTER>:value1:value2:...:valueN).
To change the default min distance of a potential variant to a splice site or an INDEL, use:
-a D:10
If a filter has more values, separate them with a ':', e.g.:
-a R:1:10:0.1
This will pool the base calls of replicates and treat all positions with:
* less than 10 reads supporting a SNV or
* variant fraction is less than 0.1
as RARE events.

All filtered positions are stored in OUTPUT_filtered. Detailed fitlering information is available in in filter_info column (See“Output is BED like“).

Output is BED like:
Header is defined as follows:
#contig	start	end	name	stat	strand	bases11	bases21	filter_info
[…]

* name:	currently: „variant“
* stat	corresponds to the statistic(p-value) of the likelihood ratio test
* strand	„.“ => unstranded
„+“ => forward
„-“ => reverse

bases(x)(y)	column contains base counts for the respective BAM file encoded as follows:
x in {1, 2} corresponds to sample
y in {1, 2, .,,,} corresponds to the replicate
base count format (A, C, G, T), e.g.: 0,0,0,10 => 10x base T

filter_info	may contain filter information (filtered output file will contain detailed info)
e.g.: Fitlered due to biased distance of variant to splice site: will have the letter 'D'
referencing the Distance filter. Letters correspond to values from command line	option „-a“ or –apply-filter

Recommended:
java -jar JACUSA.jar -c 10 -a D -T 0.3 -u DirMult-CE -r output.bed <FILES>

Using less than 10 reads is problematic because new observations havebig impact on the test-statistic.
Depending on the mapper the default value for min. mapping quality might need re-adjustment.
-u DirMult-CE has proven to be very sensitive and specific in benchmarks and read data (HEK293).
SET –build-pileup ACCORDING TO YOUR DATA!